## Slide 1: AI Detection and Processing of Starrag Sound Data
ME 597II – Midterm Presentation
Agathiya Tharun
Ayush Viswanathan
Supported by:
John Murphy
TAMS & Maijker Corp.

## Slide 2: Background
RND of AI and IoT applications
Collaboration with manufacturing companies and universities
Proprietary sensor development coupled with AI
Machine monitoring
Maijker
Maijker partner
Resolves MTConnect implementation issues
Supporting data collection initiatives
TAMS

## Slide 3: Problem Description
High-precision multifunctional machine
Requires close monitoring
Downtime at Starrag can cost millions
Rising demand in the manufacturing field
Starrag Bumotec 191 Neo Machine

## Slide 4: Project Goals
Develop a preprocessor to create data compatible with the autoencoder
Create a ML model
Test the autoencoder
Develop a functional framework to detect anomalies in sound

## Slide 5: Current Approach
System Flow Chart
Understanding Project Scope
Gathering Relevant Audio Data
Preprocess Audio .wav file dataset
Conduct Feature Extraction
Determine Normal/Abnormal Thresholds
Build and Train Machine Learning Model
Retrain/Optimize Machine Learning Model
Test ML Model
Present to Customer
Notes: The current approach can be seen through the system flow chart above. We spent the first couple of weeks setting up meetings on the project with John and understanding the project scope of the Starrag project. The next step in the process to gather the relevant audio data. In our case, it is .wav audio files gathered from the Maijker sound sensor on the LX21 machine.

## Slide 6: Current Approach
Software
  Python Libraries – Tensorflow and Keras
  Maijker Machine Learning Library
  Access to Audio .wav file datasets and melSpectrograms
Hardware
  Access to good GPU for training model
    Requires high ram and computing power
    Google Colab for Training
Identification of Requirements

## Slide 7: Autoencoder
Basic Theory
Notes: The main function of an autoencoder is to compress and replicate the input data to create a more efficient and accurate representation of data. There are essentially 2 fully-connected neural networks: the encoder and the decoder. The encoder compresses the input data into a latent-space representation, typically of lower dimensionality, capturing the most important features of the input. This compressed representation is then fed into the decoder, which attempts to reconstruct the original input data from this representation. The objective of training an autoencoder is to minimize the difference between the input and the reconstructed output, also known as reconstruction error. The main application of Autoencoders is to accurately capture the key aspects of the provided data to provide a compressed version of the input data, generate realistic synthetic data, or flag anomalies.

## Slide 8: Autoencoder
Convolutional Autoencoder
Healthy
0.014
Reconstruction
Error
Notes: Explain convolutional autoencoder here

## Slide 9: Scheduling
Discrepancies:
Changes in project scope (LX21)
Data collection issues
MAC address recognition
Updated
Notes: Things that may affect schedule. Ultimately implement into bumotec

## Slide 10: Scheduling
Discrepancies:
Changes in project scope (LX21)
Data collection issues
Grafana integration issues
MAC address recognition
Updated
Notes: Things that may affect schedule

## Slide 11: Progress
Data Preprocessing & Feature Extraction
melSpectrogram
Audio .wav file
Maijker sound sensor data gathered from TAMS cloud server
Feature extraction of a spectrogram from a WAV file using librosa library
Notes: A mel spectrogram is a visual representation of audio data in the frequency domain, particularly useful for analyzing speech and music.

## Slide 12: Progress
Convolutional Autoencoder
  Latent space size of 2
Reached a reconstruction loss of 0.0427 after 20 epochs
Lack of time led to inability to iterate training and testing of the model
Autoencoder Model

## Slide 13: Progress
Denormalized melSpectrogram data and converted to spectogram
Utilized Griffin-Lim Reconstruction to convert spectrogram into a time-series WAV file
Reconstructed spectrogram to WAV file

## Slide 14: Progress
Original Audio vs. Reconstructed Audio

## Slide 15: Progress
Normal Data vs. Abnormal Data

## Slide 16: Progress
Thresholding and MAE Graphs
MAE Reconstruction Threshold = 0.0177

## Slide 17: Project Progress
Current Stage
Understanding Project ScopeX
Gathering Relevant Audio Data
Preprocess Audio .wav file dataset
Conduct Feature Extraction
Determine Normal/Abnormal Thresholds
Build and Train Machine Learning Model
Retrain/Optimize Machine Learning Model
Test ML Model
Present to Customer

## Slide 18: Challenges
Lack of live data for the LX21
Limited time
Inability to create a dataflow to Grafana
Attempted to use local data
  Grafana network errors
  Avoided Grafana
Lack of time to retrain and test autoencoder model
Visible difference between input and reconstructed input

## Slide 19: Project Benefits
Proactive maintenance
Preemptive troubleshooting
Reduced downtime
Detailed feedback
Continuous monitoring
Optimized performance

## Slide 20: Conclusion
Final Takeaways
  melSpectrogram will require modifications to the autoencoder model
  LX21 autoencoder will be a good model for Bumotec machine
  Sound data is difficult to process
Future Improvements
  Can further refine the autoencoder model
  Create a scalable architecture to work with more machines
  Incorporate handling for live data
  Develop a Grafana dashboard to display live data
Final Takeaways and Next Steps

## Slide 21: Thank You

## Slide 22
Problem Slides
  Company Background - Applications
  Motivation for Problem
  Problem Description
    Mention the fact that we went from 191neo to LX21 to practice on the data due to delays
Proposed Approach
  Problem Scope/Project Goals
    Utilize some kind of flow chart with images
  Flow chart of current approach (keep it general and talk about auto encoder, etc.)
  Identification of Requirements (GPU, software, python libraries, datasets, etc.)
  Mention auto-encoder and how it works
  Mention 2 types of auto encoders we are considering to use (LSTM auto encoder and Convolutional auto encoder) and pros/cons
Project Planning
  Slide explaining planning (break it into stages or import Gantt chart), task distribution, and number of visits/interactions
Project Progess
  Mention what stage we are in
  Slide of data preprocessing - include melspectrogram image
  Slide of data preprocessing
  Slide on anticipated challenges
Conclusion
  Benefits on the Project - few bullet points / images that explain benefit and realistic outcome for company
  Conclusion Slide - final takeaways, future steps, etc.
Thank you
  Thank you slide