## Slide 1: Bionics Solution for Myasthenia Gravis
Agathiya, Atharva, CJ, Jake

## Slide 2: Background
Myasthenia Gravis (MG)
Inhibits neuromuscular junction and prevents neural impulses from reaching the muscle
Blocks acetylcholine receptors
Notes: What pathology have you chosen to address?
Why is this important?
Who does it affect?
Use this section to hook your audience, and make us care about what you have to say during the rest of the talk.

## Slide 3: Background
Most common in:
  Women under 40
  Men over 60
Loss of muscular function, limited facial expressions, fatigue, difficulty walking
Notes: What pathology have you chosen to address?
Why is this important?
Who does it affect?
Use this section to hook your audience, and make us care about what you have to say during the rest of the talk.

## Slide 4: Biomechanical Modeling | Pathology
Healthy and unhealthy gait10dof18musc model
Healthy
Unhealthy
Rectus femoris
Vasti
Weakened vasti muscle properties
Healthy vasti muscle properties
Weakened
Used the ‘gait10dof18musc’ model
Created a healthy and unhealthy (MG) copy
Reduced max isometric force (5000N → 500N)
Notes: How did you model your pathology, and why did you model it that way?
Used 2 models of gait10dof18musc: This model focuses on the lower extremity, and groups the vasti muscle into one (simplifies simulation), have 2 models to compare muscle performance between healthy and unhealthy
Reduced Fmax: this change reflects the muscles weakened force-generating capability (thus simulating the lack of neural signals reaching a muscle)

## Slide 5: Biomechanical Modeling | Pathology
Healthy vs unhealthy vasti muscle metabolics
Healthy vs unhealthy rectus femoris muscle metabolics
Stance phase with ground reaction force
Notes: In Figure 4, the weakened vasti muscle metabolic cost peaks during stance phase at around 0.75 seconds, where knee stabilization is crucial to handle ground reaction forces. After this phase, the weakened vasti generate less force, leading to lower metabolic demand compared to the healthy case.
Figure 5 shows the rectus femoris compensating for the vasti’s weakness. In the MG case, it peaks again during the stance phase and at swing phase, with increased activation to stabilize the knee and support forward motion.

## Slide 6: Biomechanical Modeling | Pathology
Lateral
Posterior
Modeled a path actuator in 2 configurations
Tested for 4 different max isometric forces in the actuator 7
  700N, 1000N, 2000N, 3000N
Optimized the system to reduce the effort required by the rectus femoris muscle
Computed the torque from forces and moment arm
Notes: Preliminary analysis showed Vasti muscle utilizes only about 1000N of force during normal gait, so the muscle was weakened to 500N from 5000N to realistically model MG
The isometric force values for actuator were chosen based on the vasti muscle usage in the healthy gait
Modelled a path actuator using custom Python script and then adjusted the placement in OpenSim
Frame fixation- Tibia and Femur
Moment arms were calculated using the compute Moment Arm script and for torques just multiplied forces and moment arms

## Slide 7: Biomechanical Modeling | Bionic System
Lateral
Posterior
Healthy
Assisted vs Unassisted
Notes: The plots take into account the assumed bionic system weight of 3 kg with 2.75 kg added to femur and 0.25 kg added to tibia
Rectus femoris is not utilized in normal gait and most of the load is taken by Vasti.
With reduced vasti capacity, the posterior placed actuator mimics the actual muscle usage of rectus femoris
0.8 is footflat where torque changes direction 1.2 is where again the torque changes direction in pushoffs

## Slide 8: Biomechanical Modeling | Bionic System
Lateral
Posterior
Healthy
Assisted vs Unassisted
Notes: The plots take into account the assumed bionic system weight of 3 kg with 2.75 kg added to femur and 0.25 kg added to tibia
Rectus femoris is not utilized in normal gait and most of the load is taken by Vasti.
With reduced vasti capacity, the posterior placed actuator mimics the actual muscle usage of rectus femoris

## Slide 9
Biomechanical Modeling | Bionic System
The overall metabolic cost of gait with MG with the actuator is low compared to unassisted gait, indicating that the bionic system aided in gait
The forces generated in the rectus femoris and vasti in the model with the actuator is far less than those in the model without the actuator

## Slide 10
Bionic System Design
High Level
Notes: Present your system design from a high-level.

## Slide 11
Bionic System Design
High Level
Reduce gait load
Wiring within Kevlar
Kevlar Waist Strap
Longitudinal Fins
6.7W heat dissipation
Safely operates within 48V range
U8 KV100 Motor
Motor Encoder
EMG Patches
3 patches around the thigh
Electronics
Microcontroller
Motor Driver
3 stacks of 4 for 45 min
Battery Packs
Kevlar Suit
Thermal insulation and durability
Notes: Present your system design from a high-level.

## Slide 12
Bionic System Design
High Level
Multi-stage geartrain; N = 45
Transmission
Torque Sensor
Secures bionic system to leg
Kevlar Straps
Structure and support
Aluminum Frame
Notes: Present your system design from a high-level.

## Slide 13
Kevlar Suit
Thermal insulation and durability
3 stacks of 4 for 45 min
Battery Packs
Reduce gait load
Wiring within Kevlar
Kevlar Waist Strap
Longitudinal Fins
6.7W heat dissipation
Secures bionic system to leg
Kevlar Straps
Structure and support
Aluminum Frame
EMG Patches
3 patches around the thigh
Electronics
Microcontroller
Motor Driver
Safely operates within 48V range
U8 KV100 Motor
Motor Encoder
Multi-stage geartrain; N = 45
Transmission
Torque Sensor
Notes: Present your system design from a high-level.

## Slide 14
T-Motor U8 KV100
Bionic System Design | Actuator
T-Motor U8 KV100
Multi-stage geartrain
  Transmission Ratio: 45
  9:1 and 5:1 geartrains
Power Loss = 6.7W
@ N = 45
Notes: What actuator did you choose, and why?
Played around with a few motors but ended up with the U8 KV100 motor due to its ability to operate efficiently to meet the required torque trajectory. We Started by using a random motor to see what the current and voltage requirements are, then we did an iterative process until we found a motor thats able to operate within reasonable voltage and current requirements to meet the required torque trajectory.
What is the optimal transmission ratio?
Now that we have the motor properties down, we then optimized for power loss by tuning the transmission ratio. While trying to minimize the power loss, we also have to ensure that the transmission ratio allows us to meet the peak torque required which was around 60 Nm. After doing this process, we found that a transmission ratio of 45 gives us the required peak torque, is within reasonable voltage and current requirements and also a relatively low power loss of 6.7W.
How is your transmission designed to achieve that ratio?
To achieve a transmission ratio of 45, we can use 2 sets of gears with 9:1 and 5:1 gear ratios.

## Slide 15
High Rate Discharge 3.7V 1080mAh 15C LiPo Battery
Bionic System Design | Power Supply
  3.7V, 1080 mAh, 15C
  Connected in series (13S1P)
Array of 13 High Rate Discharge LiPo batteries
Provides 48.1V and 1080 mAh capacity
15C → can draw up to 16.2 A
Each battery = 25g → total of 325g
Runtime of ~46 mins
Option for swappable batteries and/or larger batteries (e.g. 2160 mAh, 13S2P)
Notes: The power supply of the bionic system is an array of 13…
Can also add more batterues to expan

## Slide 16
Controls Flowchart
Bionic System Design | Controls
High Level:
Topical EMG sensor on rectus femoris used to control motor and apply torque
Mid Level:
Joint angle encoder
Output torque sensor
Low Level:
ADCs built into sensors, communicate to MC
Microcontroller uses data and PID control to command motor driver
Notes: For the controls of the system, from a high level a topical EMG sensor on the rectus femoris is used to control the motor and apply to to the knee joint.

## Slide 17
Bionic System Design | Controls
Low Level:
ADCs built into sensors, communicate to MC
Microcontroller uses data and PID control to command motor driver
Controls Flowchart
High Level:
Topical EMG sensor on rectus femoris used to control motor and apply torque
Mid Level:
Joint angle encoder
Output torque sensor
Notes: For the controls of the system, from a high level a topical EMG sensor on the rectus femoris is used to control the motor and apply to to the knee joint.

## Slide 18
Bionic System Design | Results
The simulation was rerun with the true calculated weight of the bionic: 1.75kg
There was negligible change in the metabolic cost or the forces in vasti and rectus femoris due to the weight change in the bionic system
Notes: This suggests we can add more weight on the femur for upto 2.75 kg (like batteries) without any significant change in the metabolic cost which could lead to extended system life

## Slide 19
Surgical Innovation
ENG instead of EMG allows for better readings of intended muscle movement
Intrafasicular electrode into the femoral nerve to read the impulses before they get blocked at the NMJ
Risk of infection
Nerve damage
Electrode displacement
Cost
Costs
Benefits
Better readings of impulses
Reduced cognitive effort
More accurate movements
Pronounced movements
Notes: What surgical techniques do you recommend be applied to improve
your system? What are the potential risks of these techniques? Do the potential benefits
outweigh the costs of invasiveness?

## Slide 20
Risk of infection
Nerve damage
Electrode displacement
Cost
Surgical Innovation
Costs
Benefits
Better readings of impulses
Reduced cognitive effort
More accurate movements
Pronounced movements

## Slide 21: 85%
5% chance of nerve damage
10% chance of electrode displacement
Notes: 85% overall success rate

## Slide 22: Thank You