## Slide 1: Multi-Robot Collaboration for 3D Concrete Printing
IE 574 – Final Project Presentation
Jorge Rojas
Kunal Mamtani
Agathiya Tharun

## Slide 2: Background
$10 trillion dollar industry
  Lack of automation
Construction robots (CoBots) are not an optimal solution
3DCP (3D Concrete Printing)
  Innovative and more optimal solution
  Growing field with many unresolved challenges

## Slide 3: Problem Definition
3DCP poses many challenges; it offers an oversimplified solution in many ways.
Often requires human intervention (sometimes dangerous) to do intricate tasks retrospectively.
  Specifically, plumbing, electrical box installation, and laying steel mesh

## Slide 4: Method
Toolpath planning
and Simulation
3D Printing Process
Rigging anchors
Delivery for assembly

## Slide 5: Method
Off-site storage of 3DCP walls
Assembly on-site of 3DCP walls

## Slide 6: Method
System Diagram

## Slide 7: Method
System Diagram
UR10 places the box in its hole

## Slide 8: Method
Toolpath planning

## Slide 9: Method
Pick and place of block outs
Calculated 0th order M00 for shape identification
Simple and robust solution ideal for easy geometries
Leveraged blob detection camera to move the Cobot arm
Notes: Calculated the Zeroth-order moment M00 to determine the shape of the fixture spot.
Very simple and robust solution that works well with simpler geometries.
Utilized the blob detection camera to move the Cobot to place corresponding shape in the fixture hole.

## Slide 10: Method
Use a Deep Learning model to choose the necessary fixture
Trained the model on three classes: Square, Cylinder, and Rectangle
Used a ResNet Model for generalization benefits; with 90% validation accuracy
Deep Learning method pick and place of block outs

## Slide 11: Main Findings
Two approaches were tested for vision sensing
  Zero order moment
  Deep learning network
M00 was sufficient for the task implemented but the DL approach needed further integration.
The descriptors approach worked well for the simple classes, but a more robust approach is needed for more complex tasks.

## Slide 12: Evaluation
Descriptors are enough for simple geometry classification
Limitations to this approach:
  Large variety of hole shapes (geometries, dimensions, and locations).
  Variable hole location
  Necessity for object detection and localization (not just classification).
  Adjustments for inline processing (coordination of time and space for both robots).
  A conveyor belt representation isn’t the most realistic
  Necessity to install a camera on the robot’s end-effector and not in a fixed position
  Necessity of sensing data fusion if complex geometries appear

## Slide 13: Conclusion
Traditional construction methods are labor-intensive and time-consuming
3DCP alleviates problems in construction
  Lack of labor force
  Reduced productivity
There still remain manual tasks that need to be completed alongside the robot printer
  Automation of such synergistic activities remains a problem
Installing the block-outs in the wall openings yields potential for automation.

## Slide 14: Contributions
Spearheaded environment and simulation development
Drove project direction
Trained deep learning model to be used
Created a classifier file
Evaluated and compiled findings
Attempted deep learning integration
Jorge Rojas Kunal Mamtani Agathiya Tharun

## Slide 15: Thank You